## Slide 1: MicroPython & ESP8266
Michael Niepel

## Slide 2
Micropython & ESP8266
ESP8266
Sensors MicroPython
MQTT
Basics Workshop
Notes: Kein Entweder-oder! Software und Hardware. Code und Kultur. Hightech und Heartbeat – wir bringen Charaktere, Kompetenzen und Ansichten zusammen. Synergien statt Silos. Dieser Ansatz greift auch unser Logo auf: Die beiden Xe in unserem Namen formen ein „&“ und symbolisieren so das Zusammenbringen unterschiedlichster Variablen.

## Slide 3: ESP8266
Cheap Wi-Fi module for IoT applications with microcontroller capability
Development board ESP-12E NodeMCU
  Wi-Fi
  4MB Flash
  USB to Serial (UART)
  11 digital I/O
  1 analog input
  Support for various languages
    C++
    JavaScript
    MicroPython
    Lisp

## Slide 4: Sersors
IR optical sensor FC-51
  Comparator LM393
  2 - 30cm range
  Input voltage 3,3 - 5V

## Slide 5: Sersors
Sound sensor
  Comparator LM393
  Input voltage 4 - 6V

## Slide 6: Sersors
Temperature sensor
  Digital sensor
  UMW DS18B20
  Range: -55 to +125 °C
  Input voltage 2,5 - 5,5V

## Slide 7: MicroPython
  Python3 implementation
  Subset of Python Standard Library
  Optimalisation for MCU
  REPL (aj WebREPL)
  HW modules
    machine
    esp
    network
    onewire
    neopixel
    dht (temperature and humidity sensors)
    ssd1306 (OLED display)
    http://docs.micropython.org/en/latest/library/index.html

## Slide 8: MQTT
The Standard for IoT Messaging
  Message Queue Telemetry Transport
  Lightweight
  Publish/Subscribe
  Low bandwidth
  TLS encryption
  OAuth authentication
  Authorization

## Slide 9: MQTT
The Standard for IoT Messaging

## Slide 10: MQTT
The Standard for IoT Messaging
  Servers/Brokers
    RabbitMQ, HiveMQ, Mosquitto, Cassandra, …
  Cloud Brokers
    HiveMQ, MyQttHub, …
  Client libraries
    Arduino / Espduino
    libemqtt, paho, mqttools, umqtt, …
  Tools
    MQTT Explorer

## Slide 11: MQTT
Versus HTTP
 | MQTT | HTTP
Architecture | Pub - Sub | Request - Response
Command Target | Topics | URIs
Underlying protocol | TCP/IP | TCP/IP
Secure connections | TLS + username/pwd (SASL support) | TLS + username/pwd (SASL support)
Client observability | Known connection status | Unknown connection status
Messaging mode | Async, event-based | Sync
Message queuing | Broker can queue | Application needs to implement
Message overhead | 2 bytes min. Header can be binary | 8 bytes min. Header is text
Message size | 256 MB max | No limit
Content type | Binary | Text
Message distribution | One to many | One to one
Reliability (QoS) | 0 (forget), 1 (at least 1), 2 (exactly 1) | Application ahs to implement

## Slide 12: MQTT
Versus HTTP Performance
 | MQTT Bytes | HTTP Bytes
Establish connection | 5572 | 2261
Disconnect | 376 (optional) | 0
For each message published | 388 | 3285
Sum for 1 message | 6336 | 5546
Sum for 10 messages | 9829 | 55,460
Sum for 100 messages | 44,748 | 554,600

## Slide 13: Basics
Flash Firmware & Test Connection & Install CP2102 drivers
  MicroPython firmware
    https://micropython.org/download/?port=esp8266
  CP210x drivers
    https://www.silabs.com/developers/usb-to-uart-bridge-vcp-drivers
  Esptool
    pip install esptool
    http://docs.micropython.org/en/latest/esp8266/tutorial/intro.html#deploying-the-firmware
  Test connection over serial
  picocom, minicom, screen (mac)
    http://docs.micropython.org/en/latest/esp8266/tutorial/repl.html
  Mu Editor
    https://codewith.mu/

## Slide 14: Basics
LED & REPL
  $ picocom /dev/tty.usbserial-0001 -b115200
> import time
> from machine import Pin
> onboard_led = Pin(4, Pin.OUT)
> onboard_led.off()
> onboard_led.on()
> while True:
> time.sleep(0.5)
> onboard_led.off()
> time.sleep(0.5)
> onboard_led.on()
> CRTL+A+X (exit picocom)

## Slide 15: Basics
IR Sensor & REPL
  $ picocom /dev/tty.usbserial-0001 -b115200
> import time
> from machine import Pin
> # 0 is “on” > ir_sensor = Pin(4, Pin.IN)
> # onboard led is reverted
> onboard_led = Pin(2, Pin.OUT)
> while True:
> if not ir_sensor.value():
> onboard_led.off()
> else:
> onboard_led.on()

## Slide 16: Basics
Sound sensor & REPL
  $ picocom /dev/tty.usbserial-0001 -b115200
> import time
> from machine import Pin
> # 0 is “on” > snd_sensor = Pin(4, Pin.IN)
> # onboard led is reverted
> onboard_led = Pin(2, Pin.OUT)
> while True:
> if not snd_sensor.value():
> onboard_led.off()
> else:
> onboard_led.on()

## Slide 17: Basics
Distance sensor & REPL
  $ picocom /dev/tty.usbserial-0001 -b115200
> from hcsr04 import HCSR04
> # HCSR04(trigger, echo)
> dist_sen = HCSR04(12, 14)
> while True:
> print(dist_sen.distance_cm())
>

## Slide 18: Basics
Temperature sensor DS18B20 & REPL
  $ picocom /dev/tty.usbserial-0001 -b115200
> import onewire
> import time, ds18x20
> from machine import Pin
> ow = onewire.OneWire(Pin(4))
> ds = ds18x20.DS18X20(ow)
> roms = ds.scan()
> while True:
> ds.convert_temp()
> time.sleep_ms(750)
> for rom in roms:
> print(ds.read_temp(rom))

## Slide 19: Basics
DS1803 Digital Potentiometer
I2C – Inter-Integrated Circuit
SDA – data wire
SCL – clock wire
Datasheet
DS1803 helper class
  $ picocom /dev/tty.usbserial-0001 -b115200
> from ds1803 import DS1803
> ds = DS1803()
> ds.set_pot0_value(100) # 0 - 255
> ds.get_pot0_value() # return value of pot0

## Slide 20: Basics
Connect Wi-Fi
  $ picocom /dev/tty.usbserial-0001 -b115200
> import network
> def connect_wifi(ssid, key):
> wlan = network.WLAN(network.STA_IF)
> wlan.active(True)
> if not wlan.isconnected():
> print('connecting to network...’)
> wlan.connect(ssid, key)
> while not wlan.isconnected():
> pass
> print('network config:', wlan.ifconfig())
>
> connect_wifi(“SSID”, ”PWD”)

## Slide 21: Basics
MQTT - Subscribe
  $ picocom /dev/tty.usbserial-0001 -b115200
  > import time
  > from umqtt.simple import MQTTClient
  >
> def msg_callback(topic, msg):
> print(topic, msg)
>
> client = MQTTClient(”esp_1”,”node02.myqtthub.com”, ssl=False, user=“esp_1”, password=“PyConSK2022”)
> client.set_callback(msg_callback)
> client.connect() # might fail
> client.subscribe(“esp_1/led”)
>
> while True:
> client.check_msg() # client.wait_msg() blocking
> time.sleep(1)

## Slide 22: Basics
MQTT - Publish
  $ picocom /dev/tty.usbserial-0001 -b115200
  > import time
  > from umqtt.simple import MQTTClient
  >
> client = MQTTClient(”esp_1”,”node02.myqtthub.com”, ssl=False, user=“esp_1”, password=“PyConSK2022”)
> client.set_callback(msg_callback)
> client.connect() # might fail
>
> client.publish(“esp_1/temp”, “25”)
Samples
  https://github.com/micropython/micropython-lib/tree/master/micropython/umqtt.simple

## Slide 23: Basics
MQTT_AS – Async version
Non-blocking MQTT
  https://github.com/peterhinch/micropython-mqtt/tree/master/mqtt_as
Build FW with mtqq_as
  https://github.com/micropython/micropython/tree/master/ports/esp8266
Sample
  IR Sensor with MQTT

## Slide 24: Basics
Uploading Files
  Uploading Files
    https://pythonforundergradengineers.com/upload-py-files-to-esp8266-running-micropython.html
    (close other serial connections before – CRTL+A+X for picocom)
    $ ampy --help
    $ ampy --port /dev/tty.usbserial-0001 --baud 115200 ls
    $ ampy --port /dev/tty.usbserial-0001 --baud 115200 put boot.py
  Boot.py
    Run on boot
  Main.py
    Main module, run after boot

## Slide 25: Basics
Back-end side (Raspberry Pi)
  Docs
    https://www.raspberrypi.com/documentation/
  Connect
    ssh pi@raspberrypi.local (pwd: PyConSK2022)
  Config
    sudo raspi-config
  Paho MQTT
    https://pypi.org/project/paho-mqtt/
  Async MQTT
    https://github.com/sbtinstruments/asyncio-mqtt

## Slide 26: Workshop
IoT Race Track
  Carrera Race Track
  ESP8266 6x
  ESP32 2x
  HC S04 2x
  IR 2x
  Temp Sensor 2x
  DS1803
  LEDs
  Button
  RaspberryPi

## Slide 27: Workshop
Racetrack
Standard racetrack
Speed based on potentiometer value
9V input

## Slide 28: Workshop
Speed Actuator with DS1803
Control speed
Sub to racetrack/speed
Accept: { „track“: 0/1, „speed“: value}
Sample Code
Schematic

## Slide 29: Workshop
Traffic Lights
Signal track state
Sub to racetrack/lights
Accept: { „command“: <cmd> }
cmd
  rsg – starting race
  blink_red – idle state
  …just anything
Sample Code
Schematic

## Slide 30: Workshop
Button
Sets the racetrack state
Pub to racetrack/button
Msg: { „time“: <time_released>}
Sample Code
Schematic

## Slide 31: Workshop
Lap Check
Notifies lap done
Pub to racetrack/lap
Msg: { „track“: <0/1>, „lap“: <time>}
Sample Code
Schematic

## Slide 32: Workshop
Speed Control
Control speed
Racetrack „brain“ translates dist -> speed
Pub to racetrack/distance
Msg: { „track“: <0/1>, „distance“: <dist_in_cm>}
Sample Code
Schematic

## Slide 33: Workshop
Overheat
Cripple speed
Racetrack „brain“ lowers speed
Pub to racetrack/overheat
Msg: { „track“: <0/1>, „temp“: <temp_in_C>}
Sample Code
Schematic

## Slide 34: Workshop
Racetrack state on RaspberryPi
  Async MQTT
State
  Idle / Running
  Track # of laps
  Track overheated status for track
Subscribe
  Distance, lap, overheat, button
Publish
  Speed, lights, sync time
Code

## Slide 35: Workshop
Leaderboard API
  Simple FastAPI App
Score model
  time, name, created
/leaderboard/
  GET list of Scores
/leaderboard/
  POST new score {“time“: <seconds>}
/leaderboard/{score_id}
  PATCH score with name {„name“: <player_name>}
Code

## Slide 36: Workshop
Leaderboard Front End
  Simple React App
Simple Name – Time Table
Poll /leaderboard/ endpoint every 2 seconds
Check for new scores (without name)
Show form to enter name when new score found
PATCH score with name
Code

## Slide 37: LINKS
ESP2866
  https://www.espressif.com/en/products/socs/esp8266
MicroPython
    https://micropython.org/
MQTT
    https://mqtt.org/
    MQTT vs. HTTP
  Github
    https://github.com/michael-niepel-exxeta/pycon-sk-2022-esp8266